## Slide 1: Operations and Project Management ELCBUS 340 16 April 2018

## Slide 2: Today’s Agenda
Class Administration – Littlefield Launch, Team Projects
Quality
Types of Variation
Control Charting
Process Capability Ratio (Cp)
Process Capability Index (Cpk)
Statistical Process Control
Continuous
Discrete
Process Capability Studies

## Slide 3: 50,000 Feet Overview of OPM
Managing Processes
Process Strategy
Process Performance & Quality
Constraint Management
Process Layout
Lean Systems
Process Analysis
Using Operations to Compete
Operations As a
Competitive Weapon
Operations Strategy
Project Management
Managing Value Chains
Supply Chain Strategy
Inventory Management
Location
Forecasting
Sales & Operations Planning
Scheduling
Resource Planning
Process Analysis
Notes: Service vs. Manufacturing
Small vs. Medium vs. Large Firms
Industry type: hightech, healthcare, aerospace, IT, etc ….

## Slide 4
Quality
A term used by customers to describe their general satisfaction with a service or product.

## Slide 5: Costs of Quality
Four major categories:
  Prevention Costs
  Appraisal Costs
  Internal Failure Costs
  External Failure Costs
Many companies spend significant time, effort, and expense on systems, training, and organizational changes to improve quality and performance of their processes. It is estimated that COQ ranges from 20 to 30 percent of gross sales.

## Slide 6: Costs of Quality
Prevention Costs are associated with preventing defects before they happen
Appraisal Costs are incurred when a firm assesses the level of performance of its processes
Internal Failure Costs result from defects that are discovered during the production of a service or product
External Failure Costs arise when a defect is discovered after the customer receives the product or service
Ethical Failure Costs are the societal and monetary costs associated with passing defective services or products to customers

## Slide 7: TQM & Six Sigma

## Slide 8: What is Total Quality Management?
Total Quality Management (TQM)
Is a quality strategy that focuses on achieving high levels of process performance and quality by stressing three principles:
Customer Satisfaction
Employee Involvement
Continuous Improvement

## Slide 9
Customer Satisfaction
  Conformance to Specifications
  Value
  Fitness for Use
  Support
  Psychological Impressions
Total Quality Management
Principles
Notes: Customer satisfaction (internal or external): when customers’ expectations have been met or exceeded.
  Conformance to specifications
    It is the processes that produced the service or product that are really being judged.
    Specifications may relate to consistent quality, on-time delivery, or delivery speed.
  Value
    How well the service or product serves its intended purpose at a price customers are willing to pay.
  Fitness for use: customer may consider the convenience of a service or the mechanical features of a product.
  Support: the service or product support may be as important to the customer as the service or product itself.
  Psychological impressions: atmosphere, image, or aesthetics

## Slide 10
Employee Involvement
  Cultural Change
    Quality at the Source
  Teams
    Employee Empowerment
      Problem-solving teams
      Special-purpose teams
      Self-managed teams
Total Quality Management
Principles
Notes: Employee involvement
  Cultural change
    Challenge is to define customer for each employee
      External customers buy the service or product.
      Internal customers are employees in the firm who rely on output of other employees. An assembly line is a chain of internal customer-supplier relationships, with an external customer purchasing the finished goods.
    Top management must motivate cultural change.
    Everyone is expected to contribute and share the view that quality control is an end to itself
    Quality at the source
  Teams
    Employee involvement is a key tactic for improving processes and quality
    Small groups of people
      Common purpose.
      Set their own performance goals and approaches
      Hold themselves accountable for success
    Three employee-empowerment approaches to teamwork
      Problem-solving teams (also called quality circles)
      Special-purpose teams
      Self-managing teams, the highest level of worker participation

## Slide 11
Continuous Improvement
  Kaizen
  Problem-solving tools
  Plan-Do-Study-Act Cycle
Total Quality Management
Principles
Notes:   Based on the Japanese concept, kaizen
  The philosophy of continually seeking ways to improve processes.
  Not unique to quality. Applies to process improvement as well.
    Getting started
      SPC training
      Make SPC a normal aspect of daily operations.
      Build work teams and employee involvement.
      Utilize problem-solving tools within the work teams.
      Develop operator ownership in the process.

## Slide 12
  Plan-Do-Study-Act Cycle
Total Quality Management
Principles
Notes:   Problem-solving process: The Deming Wheel
    Plan—select a process needing improvement, document process, analyze data, set improvement goals, discuss alternatives, assess benefits and costs, develop a plan and improvement measures.
    Do—implement plan, monitor improvements.
    Study—analyze data to evaluate effectiveness of the plan.
    Act—document and disseminate improved process as a standard procedure.

## Slide 13: What is Six Sigma?
Six Sigma
A comprehensive and flexible system for achieving, sustaining, and maximizing business success by minimizing defects and reducing variation in processes.

## Slide 14: Six Sigma Project Frameworks
DMAIC
DFSS (Define for Six Sigma)
DMADV
IDOV

## Slide 15: DMAIC
An improvement system for existing processes falling below specification and looking for incremental improvement
Define
Measure
Analyze
Improve
Control

## Slide 16: DMADV
An improvement system used to develop new processes or products at Six Sigma quality levels
Define
Measure
Analyze
Design
Verify

## Slide 17: IDOV
Used for designing a completely new product or business process to meet customer needs and specifications or to achieve Six Sigma quality levels
Identify
Design
Optimize
Verify

## Slide 18: The Tools
Six Sigma Tools
Notes: [Introduce the Tools]
Standard Work
The best combination of machines and people working together to produce a product or service at a particular point in time.
5S
5S is a workplace organization method used to assure work can be done effectively and efficiently.
SIPOC
SIPOC is a tool that summarizes the inputs, outputs and steps of one or more processes in table form.
RACI
RACI is a method to identify the roles and responsibilities of participants in a cross organizational team.
5Ys
Statistics
Waste
Worker Realignment
Workplace Reorganization
DIG
CAPA
Affinity
Fishbone
Setup Reduction
Visual Controls
Small Lots
Kanban
A3
1-Piece Flow
SPC
Kaizen
Cycle Time Reduction
TPM
FMEA
DOE
Project Management
Reengineering
Six Sigma Project
Balanced Scorecard
QFD
Hoshin Planning
VOC

## Slide 19: Six Sigma Certifications
Master Black Belt
Black Belt
Green Belt
Yellow Belt
Certifying Organizations?

## Slide 20: Acceptance Sampling
Acceptance Sampling
  The application of statistical techniques to determine if a quantity of material from a supplier should be accepted or rejected based on the inspection or test of one or more samples.
Acceptable Quality Level
  The quality level desired by the consumer.
Acceptance Sampling

## Slide 21: Acceptance Sampling
Firm A uses TQM or Six Sigma to achieve internal process performance
Supplier uses TQM or Six Sigma to achieve internal process performance
Yes
No
Yes
No
Fan motors
Fan blades
Accept blades?
Supplier
Manufactures fan blades
TARGET: Firm A’s specs
Accept motors?
Motor sampling
Blade sampling
Firm A
Manufacturers furnace fan motors
TARGET: Buyer’s specs
Buyer
Manufactures furnaces

## Slide 22: Six Sigma Approach
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Process average OK; too much variation
Process variability OK; process off target
Process on target with low variability
Reduce spread
Center process
X
X
X
X
X
X
X
X
X

## Slide 23: Statistical Process Control

## Slide 24: Statistical Process Control (SPC)
SPC
  The application of statistical techniques to determine whether a process is delivering what the customer wants.
Performance Measurements
  Variables (Continuous) - Characteristics that can be measured.
  Attributes (Discrete) - Characteristics that can be counted.

## Slide 25
Statistical Process Control (SPC)
A process that is in statistical control:
  Is stable and predictable
  Variation will be limited to an expected range
  But still may not be capable
A process that is out of statistical control:
  Is unstable and unpredictable
  Variation will not be limited to the expected range
  Variation may be extreme

## Slide 26: Types of Variation
Common cause
Variation that is random, unidentifiable and unavoidable
Special cause
Variation that can be identified and eliminated

## Slide 27: Effects of Special Cause Variation on the Process Distribution

## Slide 28: Control Charts
Time-ordered diagram used to determine whether observed variations are abnormal

## Slide 29: Control Charting
A control chart always has a central line for the average, an upper line for the upper control limit and a lower line for the lower control limit.
By comparing current data to these lines, one can make conclusions about whether the process variation is in control or out of control (special cause variation)
Variable data control charts use two charts with attribute data using one chart
Notes: [Explain]
Describe the anatomy of a control chart – use the bullets as a guideline for your explanation.
[Draw this on the Board]
[Insert graphic from supplemental PPT, slide 7]
Remember the Galton box?
If you turn the SPC on its end and shook all of the points to the bottom, you would be a Probability Density Function (PDF) that would appear to be a normal distribution.
[Next Slide]
Control charting process

## Slide 30: Types of Control Charts
Variable Data Control Charts
X-bar Chart – Measures whether the process is generating output consistent with a target value.
R Chart – Measures the variability of the process.
S Chart – Measures the Standard Deviation of the process.
Attribute Data Control Charts
p-chart – Measures the proportion of defective services of products in a process.
c-chart – Measures the proportion of defects in one service or product.

## Slide 31: Continuous Control Charts Charts R Charts S Charts
Notes: [Explain]
Describe the anatomy of a control chart – use the bullets as a guideline for your explanation.
[Draw this on the Board]
[Insert graphic from supplemental PPT, slide 7]
Remember the Galton box?
If you turn the SPC on its end and shook all of the points to the bottom, you would be a Probability Density Function (PDF) that would appear to be a normal distribution.
[Next Slide]
Control charting process

## Slide 32
- Chart
Data are collected in a face-and-plunge operation done on a lathe. The dimension being measured is the groove inside diameter (ID), which has a tolerance of 7.125 ± 0.010. Four parts are measured every hour. These values have been entered in the table below.

## Slide 33: Chart Control Limits
=
=
Where:
= the central line of the chart
= a constant to provide three-sigma limits for the sample mean

## Slide 34: Calculating Control Chart Factors

## Slide 35: Chart Control Limits
=
=

## Slide 36: Plot data over time
Centerline =

## Slide 37: Upper and Lower Control Limits
LCL
UCL

## Slide 38
=
=
Where:
= average of several R values and the central line of the R control chart
, = constants that provide three standard deviation limits for the given sample size
R-Chart
Control Limits

## Slide 39: Calculating Control Chart Factors

## Slide 40
R-Chart
Control Limits
=
= 2.282(0.0037) = 0.008443
=
= 0(0.0037) = 0

## Slide 41
Plot the Range of each subgroup overtime, the calculated value is the centerline.
R-Chart

## Slide 42: Variation and out of control data points
Common Cause Variation
Out-of-control point (Special Cause)
Time plot of sequential process measurements

## Slide 43: Example
Sample Number | 1 | 2 | 3 | 4 | 5 |  | 
1 | 0.5014 | 0.5022 | 0.5009 | 0.5027 | 0.5045 |  | 
2 | 0.5021 | 0.5041 | 0.5024 | 0.5020 | 0.5062 |  | 
3 | 0.5018 | 0.5026 | 0.5035 | 0.5023 | 0.5054 |  | 
4 | 0.5008 | 0.5034 | 0.5024 | 0.5015 | 0.5047 |  | 
5 | 0.5041 | 0.5056 | 0.5034 | 0.5047 | 0.5043 |  | 
 | 0.50204 | 0.50358 | 0.50252 | 0.50264 | 0.50502 |  | 0.50316
R | 0.0033 | 0.0034 | 0.0026 | 0.0032 | 0.0019 |  | 0.00288
The management of West Allis Industries is concerned about the production of a special metal screw used by several of the company’s largest customers. The diameter of the screw is critical to the customers. Data from five samples appear in the accompanying table. The sample size is 5. Is the process in statistical control?

## Slide 44
=
0.5032 + 0.577(0.0029) = 0.5048
=
0.5032 – 0.577(0.0029) = 0.5015
Example
Compute the mean for each sample and the control limits.

## Slide 45
Process average is NOT in statistical control.
Example

## Slide 46
  Compute the range for each sample and the control limits
= = 2.114(0.0029) = 0.0061
= = 0(0.0029) = 0
Example

## Slide 47
Process variability is in statistical control.
Example

## Slide 49
=
=
Where:
= average of several Stdev values and the central line of the S control chart
, = constants that provide three standard deviation limits for the given sample size
S-Chart
Control Limits

## Slide 50
S - Chart
Subgroup | Obs 1 | Obs 2 | Obs 3 | Obs 4 | Obs 5 | Obs 6 | Obs 7 | Obs 8 | Obs 9 | Obs 10 | 
1 | 46.8204 | 58.8572 | 67.7175 | 51.3078 | 53.3025 | 51.3258 | 59.0268 | 49.9933 | 47.086 | 60.4783 | 
2 | 53.9847 | 47.4005 | 59.1598 | 57.2251 | 57.3207 | 50.4045 | 54.8046 | 55.7574 | 58.8662 | 59.2083 | 
3 | 52.4315 | 63.2146 | 61.4096 | 59.342 | 57.4605 | 53.7083 | 57.0489 | 58.4325 | 48.5544 | 61.4105 | 
4 | 50.9712 | 53.4314 | 52.9449 | 66.827 | 43.9849 | 67.8154 | 57.4312 | 44.3194 | 60.5493 | 59.6383 | 
5 | 62.0421 | 57.1784 | 60.1955 | 56.4687 | 64.9641 | 52.9195 | 48.6739 | 56.3773 | 60.3216 | 58.9171 | 
6 | 53.1269 | 58.374 | 63.7938 | 50.8965 | 52.4253 | 52.696 | 64.2078 | 65.9364 | 55.8426 | 54.478 | 
7 | 55.0507 | 53.8931 | 51.8424 | 68.7073 | 50.173 | 58.0991 | 59.3456 | 57.9232 | 69.2396 | 60.2033 | 
8 | 54.3315 | 52.3679 | 65.2346 | 62.6795 | 61.5929 | 54.0084 | 61.4465 | 58.4423 | 55.7608 | 54.1888 | 
9 | 59.9584 | 59.1762 | 51.5629 | 63.0753 | 59.4856 | 63.2215 | 50.8982 | 62.4343 | 49.4303 | 48.9902 | 
10 | 54.0402 | 56.3253 | 53.3773 | 54.7368 | 59.8292 | 54.6631 | 62.2161 | 61.5533 | 66.2283 | 63.0929 | 
11 | 57.2273 | 65.8816 | 67.9839 | 51.7812 | 63.3054 | 56.5156 | 54.5318 | 54.4049 | 54.6459 | 52.6297 | 
12 | 51.5133 | 61.0216 | 61.2776 | 62.1072 | 56.1983 | 54.805 | 59.083 | 58.8301 | 51.2939 | 54.9033 | 
13 | 41.6784 | 46.7246 | 90.9593 | 57.7698 | 57.6619 | 53.9903 | 47.1248 | 50.2183 | 52.0052 | 57.2942 | 
14 | 52.8303 | 42.4179 | 58.0054 | 60.1385 | 59.9954 | 60.5936 | 49.6827 | 68.2645 | 53.5693 | 60.6435 | 
15 | 58.1128 | 53.4343 | 49.8567 | 53.3065 | 48.6588 | 53.4726 | 61.1457 | 61.6733 | 54.4246 | 51.8054 | 
16 | 59.4674 | 66.2816 | 71.1186 | 63.6602 | 65.4012 | 53.2372 | 55.0633 | 46.6954 | 57.0477 | 61.8819 | 
17 | 63.6288 | 47.3453 | 45.6509 | 40.2198 | 51.7382 | 51.0804 | 56.4197 | 57.7979 | 65.3047 | 66.539 | 
18 | 59.5853 | 50.9825 | 56.2445 | 103.441 | 52.6224 | 63.7297 | 43.3771 | 58.7982 | 59.8339 | 57.9202 | 
19 | 57.8042 | 49.2275 | 56.9069 | 55.4057 | 60.342 | 62.0972 | 57.2 | 38.6509 | 61.459 | 59.144 | 
20 | 53.2788 | 62.1238 | 48.7058 | 58.0984 | 52.3153 | 56.8277 | 53.3615 | 64.6894 | 56.0133 | 56.9455 | 
21 | 61.0891 | 52.2114 | 55.0061 | 50.2427 | 55.6495 | 53.7419 | 63.6856 | 56.5452 | 55.6084 | 67.2915 | 
22 | 47.6385 | 62.0744 | 71.2102 | 64.6661 | 58.1218 | 56.8151 | 62.913 | 53.8949 | 64.6937 | 53.5819 | 
23 | 46.1471 | 57.2321 | 60.0446 | 59.5476 | 54.4676 | 48.8446 | 57.6602 | 58.5467 | 65.4449 | 50.6271 | 
24 | 53.1199 | 52.4063 | 53.1227 | 52.1897 | 56.6952 | 53.0823 | 61.1469 | 50.5565 | 56.9315 | 60.0423 | 
25 | 55.3156 | 60.7648 | 55.0855 | 56.2381 | 60.3981 | 61.7266 | 69.0841 | 51.4446 | 58.1248 | 50.136 | 
 | 54.44778 | 55.61393 | 59.53668 | 59.20314 | 56.56439 | 55.97686 | 57.06316 | 56.08721 | 57.5312 | 57.67965 | 56.9704
Stdev | 5.286458 | 6.28949 | 9.49476 | 11.10656 | 5.147585 | 4.750668 | 5.9335 | 6.835565 | 5.76572 | 4.830527 | 6.544084
Subgroup | Obs 1 | Obs 2 | Obs 3 | Obs 4 | Obs 5 | Obs 6 | Obs 7 | Obs 8 | Obs 9 | Obs 10 | 
1 | 46.8204 | 58.8572 | 67.7175 | 51.3078 | 53.3025 | 51.3258 | 59.0268 | 49.9933 | 47.086 | 60.4783 | 
2 | 53.9847 | 47.4005 | 59.1598 | 57.2251 | 57.3207 | 50.4045 | 54.8046 | 55.7574 | 58.8662 | 59.2083 | 
3 | 52.4315 | 63.2146 | 61.4096 | 59.342 | 57.4605 | 53.7083 | 57.0489 | 58.4325 | 48.5544 | 61.4105 | 
4 | 50.9712 | 53.4314 | 52.9449 | 66.827 | 43.9849 | 67.8154 | 57.4312 | 44.3194 | 60.5493 | 59.6383 | 
5 | 62.0421 | 57.1784 | 60.1955 | 56.4687 | 64.9641 | 52.9195 | 48.6739 | 56.3773 | 60.3216 | 58.9171 | 
6 | 53.1269 | 58.374 | 63.7938 | 50.8965 | 52.4253 | 52.696 | 64.2078 | 65.9364 | 55.8426 | 54.478 | 
7 | 55.0507 | 53.8931 | 51.8424 | 68.7073 | 50.173 | 58.0991 | 59.3456 | 57.9232 | 69.2396 | 60.2033 | 
8 | 54.3315 | 52.3679 | 65.2346 | 62.6795 | 61.5929 | 54.0084 | 61.4465 | 58.4423 | 55.7608 | 54.1888 | 
9 | 59.9584 | 59.1762 | 51.5629 | 63.0753 | 59.4856 | 63.2215 | 50.8982 | 62.4343 | 49.4303 | 48.9902 | 
10 | 54.0402 | 56.3253 | 53.3773 | 54.7368 | 59.8292 | 54.6631 | 62.2161 | 61.5533 | 66.2283 | 63.0929 | 
11 | 57.2273 | 65.8816 | 67.9839 | 51.7812 | 63.3054 | 56.5156 | 54.5318 | 54.4049 | 54.6459 | 52.6297 | 
12 | 51.5133 | 61.0216 | 61.2776 | 62.1072 | 56.1983 | 54.805 | 59.083 | 58.8301 | 51.2939 | 54.9033 | 
13 | 41.6784 | 46.7246 | 90.9593 | 57.7698 | 57.6619 | 53.9903 | 47.1248 | 50.2183 | 52.0052 | 57.2942 | 
14 | 52.8303 | 42.4179 | 58.0054 | 60.1385 | 59.9954 | 60.5936 | 49.6827 | 68.2645 | 53.5693 | 60.6435 | 
15 | 58.1128 | 53.4343 | 49.8567 | 53.3065 | 48.6588 | 53.4726 | 61.1457 | 61.6733 | 54.4246 | 51.8054 | 
16 | 59.4674 | 66.2816 | 71.1186 | 63.6602 | 65.4012 | 53.2372 | 55.0633 | 46.6954 | 57.0477 | 61.8819 | 
17 | 63.6288 | 47.3453 | 45.6509 | 40.2198 | 51.7382 | 51.0804 | 56.4197 | 57.7979 | 65.3047 | 66.539 | 
18 | 59.5853 | 50.9825 | 56.2445 | 103.441 | 52.6224 | 63.7297 | 43.3771 | 58.7982 | 59.8339 | 57.9202 | 
19 | 57.8042 | 49.2275 | 56.9069 | 55.4057 | 60.342 | 62.0972 | 57.2 | 38.6509 | 61.459 | 59.144 | 
20 | 53.2788 | 62.1238 | 48.7058 | 58.0984 | 52.3153 | 56.8277 | 53.3615 | 64.6894 | 56.0133 | 56.9455 | 
21 | 61.0891 | 52.2114 | 55.0061 | 50.2427 | 55.6495 | 53.7419 | 63.6856 | 56.5452 | 55.6084 | 67.2915 | 
22 | 47.6385 | 62.0744 | 71.2102 | 64.6661 | 58.1218 | 56.8151 | 62.913 | 53.8949 | 64.6937 | 53.5819 | 
23 | 46.1471 | 57.2321 | 60.0446 | 59.5476 | 54.4676 | 48.8446 | 57.6602 | 58.5467 | 65.4449 | 50.6271 | 
24 | 53.1199 | 52.4063 | 53.1227 | 52.1897 | 56.6952 | 53.0823 | 61.1469 | 50.5565 | 56.9315 | 60.0423 | 
25 | 55.3156 | 60.7648 | 55.0855 | 56.2381 | 60.3981 | 61.7266 | 69.0841 | 51.4446 | 58.1248 | 50.136 | 
 | 54.44778 | 55.61393 | 59.53668 | 59.20314 | 56.56439 | 55.97686 | 57.06316 | 56.08721 | 57.5312 | 57.67965 | 
Stdev | 5.286458 | 6.28949 | 9.49476 | 11.10656 | 5.147585 | 4.750668 | 5.9335 | 6.835565 | 5.76572 | 4.830527 | 

## Slide 51: Calculating Control Chart Factors

## Slide 52: Chart Control Limits when using large sample sizes (S Chart)
=
=

## Slide 53
S-Chart
Control Limits
=
= 1.436(6.5441) = 9.3973
=
= 0.564(6.5441) = 3.6909

## Slide 54
Chart: X-Bar: Stacked Data (Y)
 | 54.4478 | 55.6139 | 59.5367 | 59.2031 | 56.5644 | 55.9769 | 57.0632 | 56.0872 | 57.5312 | 57.6796
 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704 | 56.9704
 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028 | 53.0028
 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938 | 60.938
Chart: S: Stacked Data (Y)
 | 5.2865 | 6.2895 | 9.4948 | 11.1066 | 5.1476 | 4.7507 | 5.9335 | 6.8356 | 5.7657 | 4.8305
 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441 | 6.5441
 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696 | 3.696
 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922 | 9.3922

## Slide 55: Control Chart Evaluation
Control Chart Rules
Rule Name | Out of Control Condition | Chart Type | 
 |  | Variables | Attributes
Beyond Limits | One or more points beyond the control limits | X | X
Zone C | 9 or more consecutive points on one side of the average (in Zone C or beyond) | X | X
Trend | 7 consecutive points trending up or trending down | X | X
Over-control | 14 consecutive points alternating up and down | X | X
Zone A | 2 out of 3 consecutive points in Zone A or beyond | X | 
Zone B | 4 out of 5 consecutive points in Zone B or beyond | X | 
Stratification | 15 consecutive points in Zone C | X | 
Mixture | 8 consecutive points with no points in Zone C | X | 

## Slide 56: Discrete Control Charts c-charts np-charts

## Slide 57: Control Charts for Attributes Data c-chart
c-charts count the number of defects per unit of service encounter
The underlying distribution is the Poisson distribution
The mean of the distribution is and the standard deviation is .

## Slide 58: c-chart example
The Woodland Paper Company produces paper for the newspaper industry. As a final step in the process, the paper passes through a machine that measures various product quality characteristics. When the paper production process is in control, it averages 20 defects per roll.
a. Set up a control chart for the number of defects per roll. For this example, use two-sigma control limits.
b. Five rolls had the following number of defects: 16, 21, 17, 22, and 24, respectively. The sixth roll, using pulp from a different supplier, had 5 defects. Is the paper production process in control?

## Slide 59: c-chart example
a. The average number of defects per roll is 20. Therefore:

## Slide 60: Example 5.4
The process is out of control due to Sample 6.
c-chart example
Chart: C - Defects
 | 16 | 21 | 17 | 22 | 24 | 5
 | 20 | 20 | 20 | 20 | 20 | 20
 | 11.06 | 11.06 | 11.06 | 11.06 | 11.06 | 11.06
 | 28.94 | 28.94 | 28.94 | 28.94 | 28.94 | 28.94
However, sample 6 is from a new supplier and results in a better product.

## Slide 61: np-chart
np-charts are used to control the proportion defective
Sampling involves yes/no decisions so the underlying distribution is the binomial distribution

## Slide 62: np-chart

## Slide 63: np-chart example
A Test was conducted to determine the presence of the Rh factor in 13 samples of donated blood. The results of the test are given in the table on the next slide.
Using three-sigma control limits, is the accuracy of the blood testing process in statistical control?

## Slide 64: np-chart example

## Slide 65: Example 5.3
189
1614
= = 0.1171
p =
Total defectives
Total number of observations
Calculate the sample proportion defective and plot each sample proportion defective on the chart.
np-chart example

## Slide 66: np-chart example

## Slide 67: np-chart example
The process is in statistical control.

## Slide 68: Control Chart Evaluation
Control Chart Rules
Rule Name | Out of Control Condition | Chart Type | 
 |  | Variables | Attributes
Beyond Limits | One or more points beyond the control limits | X | X
Zone C | 9 or more consecutive points on one side of the average (in Zone C or beyond) | X | X
Trend | 7 consecutive points trending up or trending down | X | X
Over-control | 14 consecutive points alternating up and down | X | X
Zone A | 2 out of 3 consecutive points in Zone A or beyond | X | 
Zone B | 4 out of 5 consecutive points in Zone B or beyond | X | 
Stratification | 15 consecutive points in Zone C | X | 
Mixture | 8 consecutive points with no points in Zone C | X | 

## Slide 69
Continuous
Discrete
n = 1 n = 2 to 9 n = 10+
I-MR
chart
Xbar-R chart
Xbar-S chart
Defects
Defectives
Yes No
c chart
u chart
Yes No
np chart
p chart
Type of Data
Subgroup Size
Defectives or Defects
Constant Sample Size
Constant Sample Size
Basic Control Charting Decision Tree

## Slide 70
Process Capability – The ability of the process to meet the design specification for a service or product
Process Capability

## Slide 71: Process Capability
20
25
30
Minutes
Upper
specification
Lower
specification
Nominal
value
(a) Process is capable
Process distribution

## Slide 72: Process Capability
20
25
30
Minutes
Upper
specification
Lower
specification
Nominal
value
(b) Process is not capable
Process distribution

## Slide 73: Process Capability
Lower
specification
Mean
Upper
specification
Nominal value
Six sigma
Four sigma
Two sigma
Process Capability

## Slide 74: Process Capability Ratio
A test to see if the process variability is capable of producing output within a product’s specifications.
Cp =
Upper specification – Lower specification
6σ
Process Capability Ratio

## Slide 75: Example 5.5
The intensive care unit lab process has an average turnaround time of 26.2 minutes and a standard deviation of 1.53 minutes.
The nominal value for this service is 25 minutes ± 5 minutes.
Is the lab process capable of four sigma-level performance?
Upper specification = 30 minutes
Lower specification = 20 minutes
Average service = 26.2 minutes
 = 1.53 minutes
Process Capability Ratio

## Slide 76: Example 5.5
Process did not meet 4-sigma level of 1.33
Process Capability Ratio

## Slide 77: Process Capability Index
Measures how well a process is centered and whether the variability is acceptable
Cpk = Minimum of ,
x – Lower specification
3σ
Upper specification – x
3σ
where
σ = standard deviation of the process distribution
Process Capability Index

## Slide 78: Example 5.5
The intensive care unit lab process has an average turnaround time of 26.2 minutes and a standard deviation of 1.53 minutes.
The nominal value for this service is 25 minutes ± 5 minutes.
Is the lab process capable of four sigma-level performance?
Upper specification = 30 minutes
Lower specification = 20 minutes
Average service = 26.2 minutes
 = 1.53 minutes
Process Capability Index

## Slide 79: Example 5.5
Cpk = Minimum of 26.2 – 20 , 30 – 26.2
3 ( 1.53) 3( 1.53)
Cpk = Minimum of ,
Process does not meets 4-sigma level of 1.33
Cpk = Minimum of 1.35, 0.83
Cpk = 0.83
Process Capability Index

## Slide 80: Example 5.5
New Data is collected:
Upper specification = 30 minutes
Lower specification = 20 minutes
Average service = 26.1 minutes
 = 1.20 minutes
Process meets 4-sigma level of 1.33 for variability
Process Capability Ratio

## Slide 81: Example 5.5
Cpk = Minimum of 26.1 – 20 , 30 – 26.1
3 ( 1.20) 3 ( 1.20)
Cpk = 0.59
Process does not meets 4-sigma level of 1.33
Process Capability Index
Cpk = Minimum of ,
x – Lower specification
3σ
Upper specification – x
3σ
Cpk = Minimum of 0.59 1.08

## Slide 82: Example 5.5
Process Capability Failure Rates